## Slide 1
IOT-ENABLED INTELLIGENT
SEWER MONITORING AND
FLOOD RISK EARLY-WARNING
SYSTEM
Department of Mechanical Engineering
BHUVANAN M | ARAVINTH R | AMBIKA B | DHARANESHWARAN B
KNOWLEDGE INSTITUTE OF TECHNOLOGY TEAM - 9

## Slide 2
KNOWLEDGE INSTITUTE OF TECHNOLOGY
IOT-ENABLED INTELLIGENT SEWER MONITORING AND FLOOD RISK EARLY-WARNING SYSTEM
2
Objective: To continuously monitor drainage and sewage conditions using real-time IoT sensor data for early blockage and flood-risk warning. Solution: An integrated system using an ESP8266 NodeMCU, HC-SR04 ultrasonic sensor, YF-S201 water-flow sensor, rain sensor module, I2C LCD, and a Wi-Fi web dashboard. Impact: Reduces manual inspection, enables early detection of blockage and overflow, and supports timely preventive maintenance for safer urban drainage.
ISOMETRIC VIEW
PROTOTYPE

## Slide 3
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Engineering Design Process
3
1
Problem
Identification
2
Requirement
Analysis
3
Concept
Development
4
System
Design
5
Prototype
Development
6
Testing &
Validation
7
Optimization
8
Final
Evaluation

## Slide 4
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Process Table
4
Phase | Activity | Outcome
Water-Level Sensing | Ultrasonic sensor (HC-SR04) measures distance to the water surface | Water level data sent to ESP8266
Flow Sensing | YF-S201 flow sensor generates pulses proportional to water movement | Flow rate calculated; restriction identified
Rain Sensing | Rain sensor detects water droplets on its sensing plate | Rainfall status identified for flood-risk check
Data Processing | ESP8266 compares sensor readings with predefined threshold values | Drainage status determined (Normal / Blockage / Overflow)
Data Display | 16×2 I2C LCD shows water level, flow, rain status, and system status | Real-time local monitoring enabled
Remote Monitoring | ESP8266 sends processed data to the web dashboard over Wi-Fi | Remote monitoring and warning alerts via dashboard

## Slide 5
KNOWLEDGE INSTITUTE OF TECHNOLOGY
List of Activities
5
Literature Survey: Reviewed existing IoT-based drainage and flood monitoring systems and identified research gaps.
Component Selection & Procurement: Selected ESP8266, HC-SR04, YF-S201, rain sensor, and LCD based on cost, accuracy, and compatibility.
Circuit Design & Assembly: Interfaced all sensors with the ESP8266 NodeMCU and assembled the wiring on the prototype.
Firmware Development: Programmed the ESP8266 using Arduino IDE with threshold-based condition logic.
Dashboard Development: Built a web-based dashboard for live monitoring, warning display, and CSV data export.
Prototype Fabrication & Testing: Built the drainage-channel prototype and validated it under normal, blockage, overflow, and rainfall conditions.
PROTOTYPE BUILD

## Slide 6
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Activity Duration Table
6
Activity ID | Task Description | Duration
A1 | Literature Survey & Requirement Gathering | 1 Week
A2 | Component Selection & Procurement | 1 Week
A3 | Sensor Interfacing & Circuit Wiring | 2 Weeks
A4 | Arduino IDE Programming & Threshold Logic | 2 Weeks
A5 | Web Dashboard Development | 2 Weeks
A6 | Prototype Fabrication & Assembly | 2 Weeks
A7 | System Integration & Testing | 2 Weeks

## Slide 7
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Activity Precedence Table
7
Activity | Preceded By | Logic
Component Procurement | Literature Survey | Requirements must be finalized before ordering parts
Circuit Wiring | Component Procurement | Components must be available before assembly
Firmware Programming | Circuit Wiring | Hardware must be wired before code can be tested
Dashboard Development | Firmware Programming | Data format must be defined before building the dashboard
Prototype Fabrication | Circuit Wiring | Physical structure is built around the wired components
System Testing | Dashboard Development, Prototype Fabrication | Integration testing follows once all subsystems are ready

## Slide 8
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Glossary
8
IoT (Internet of Things):
Network of physical devices connected for real-time data exchange over the internet.
ESP8266:
Low-cost Wi-Fi enabled microcontroller used as the main control and communication unit.
HC-SR04:
Ultrasonic distance sensor used to measure the water level inside the drainage channel.
YF-S201:
Hall-effect water-flow sensor that generates pulses proportional to the flow rate.
Rain Sensor Module:
Sensor that detects the presence and intensity of rainfall for flood-risk assessment.
Threshold Value:
Predefined limit used by the ESP8266 to classify drainage conditions as normal or abnormal.

## Slide 9
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Science Principles
9
Ultrasonic Echo Principle:
Distance is measured from the time taken for a transmitted ultrasonic wave to reflect off the water surface and return to the sensor.
Hall-Effect Sensing:
A rotor inside the flow sensor generates electrical pulses proportional to the rate of water flow as it turns.
Conductivity-Based Sensing:
The rain sensor's output changes as water bridges the conductive tracks on its exposed sensing plate.
Wireless Communication:
The ESP8266 uses 802.11 Wi-Fi (TCP/IP) to transmit sensor data to the web dashboard in real time.

## Slide 10
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Concept Rules & Laws
10
Threshold Rule: A warning is triggered only when water level or flow rate crosses a predefined critical limit.
Automation Rule: Sensor → ESP8266 → LCD/Dashboard data flow requires no manual intervention.
Feedback Monitoring Law: Continuous sensor feedback allows the system to reclassify drainage status in real time as conditions change.
IoT Data Principle: Real-time sensor data streams continuously to the web dashboard for remote access, warnings, and CSV logging.

## Slide 11
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Constants & Variables
11
CONSTANTS
VARIABLES
ESP8266 Clock Speed: 80 MHz
Sensor Supply Voltage: 3.3 – 5 V
HC-SR04 Operating Voltage: 5 V
LCD Size: 16 × 2 (I2C interface)
Total Project Cost: ₹ 2,820 (approx.)
Water Level (cm): varies with drainage condition
Flow Rate (L/min): changes with water movement
Rainfall Status: ON / OFF from rain sensor
Drainage Status: Normal / No Flow / Blockage
Overflow / Flood Risk

## Slide 12
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Key Equations
12
System Logic Model
Sensor Readings → ESP8266 Processing → Threshold Check → LCD / Dashboard Update → Warning Trigger
Water-Level Calculation: Water Level = Sensor Mounting Height − Measured Distance (from HC-SR04 echo time)
Blockage Decision: IF (Water Level > High Threshold) AND (Flow Rate < Low Threshold) THEN Blockage Warning
Flood-Risk Decision: IF (Water Level > Critical Threshold) AND (Rain = Detected) THEN Flood-Risk Alert
Sensor Accuracy (tested): Water-level measurement accuracy ≈ ± 0.2 cm (Table 8.1 trial results)

## Slide 13
KNOWLEDGE INSTITUTE OF TECHNOLOGY
What-If Analysis
13
Q1: What if Wi-Fi disconnects?
The system continues local operation; the LCD keeps displaying live readings while the ESP8266 automatically retries the connection.
Q2: What if a sensor gives a faulty reading?
Threshold-based logic reduces false alarms; the affected sensor should be inspected and recalibrated periodically.
Q3: What if the power supply fails?
Monitoring stops until power is restored; a battery backup can be added to prevent gaps in monitoring.
Q4: What if the drainage size or flow rate changes?
Threshold values in the firmware can be updated for different pipe or channel dimensions.

## Slide 14
KNOWLEDGE INSTITUTE OF TECHNOLOGY
Conclusion
14
The IoT-Enabled Intelligent Sewer Monitoring and Flood Risk Early-Warning System successfully demonstrates a low-cost, real-time drainage monitoring approach using an ESP8266 NodeMCU with ultrasonic, water-flow, and rain sensors. The prototype accurately measures water level, detects flow restrictions, and identifies rainfall to classify drainage status as Normal, No Flow, Blockage, Overflow, or Flood Risk. A 16×2 I2C LCD provides local monitoring, while a Wi-Fi web dashboard delivers live readings, graphs, warning alerts, and CSV data export for remote monitoring.Testing confirmed reliable detection of blockage and overflow conditions, validating the system as a practical, scalable foundation for smart-city drainage and flood-prevention networks.
THANK YOU